## Slide 1
ECE6880 Project
Audio Adaptive Noise Cancellation Using LMS Algorithm
Zeyu Liu

## Slide 2
s + n
Filter
−
n0
s + n
+
∑
Filter
The usual method of estimating noisy signal

## Slide 3
FIR adaptive filter
LMS adaptive filter
Noise canceller
System output
error
e
−
∑
Filter output
y,
n0
Reference input
+
d = s + n
Primary input
Signal source
Noise source
Adaptive Noise Canceller using LMS algorithm
is uncorrelated with and :

## Slide 4
The simplest LMS algorithm
1.Weights evaluation:
2.Estimation error (In this project, error is the desired output):
3.Filter output:

## Slide 5
AR model
AR model describes the relationship between current and historical values.
MA model
MA model describes the error accumulation of the autoregressive part.
: white noise
: white noise

## Slide 6
Listening Time
USE MATLAB TO SHOW THE PLOT AND SOUND

## Slide 7
M = 10 | Step size µ | iterations | MSE | iterations | MSE | iterations | MSE
 | 0.001 | 200 | 2.4945 | 15000 | 0.0373 | 50000 | 0.0112
 | 0.005 | 200 | 0.5892 | 15000 | 0.0079 | 50000 | 0.0024
 | 0.1 | 200 | 1.0023 | 15000 | 0.0134 | 50000 | 0.0040
µ = 0.005 | taps M | iterations | MSE | iterations | MSE | iterations | MSE
 | 5 | 200 | 1.2461 | 15000 | 0.0116 | 50000 | 0.0050
 | 10 | 200 | 0.5892 | 15000 | 0.0079 | 50000 | 0.0024
 | 30 | 200 | 0.6349 | 15000 | 0.0085 | 50000 | 0.0025

## Slide 8
REFERENCES
Dhobale, S., Boldhan, V., & Burange, R. A. (2013). Implementation of adaptive noise canceller using lms algorithm. In National Conference on Innovative Paradigms in Engineering & Technology.
Mills, T. (1990). Time series techniques for economistscambridge university press. Cambridge et al, 52, 68.
Ross, L., & Russ, J. C. (2011). The image processing handbook. Microscopy and Microanalysis, 17(5), 843.
Chhikara, J., & Singh, J. (2012). Noise cancellation using adaptive algorithms. International Journal of Modern Engineering Research, 2(3), 792-795.
Singh, A. (2001). Adaptive noise cancellation. Dept. of Electronics & Communication, Netaji Subhas Institute of Technology, 1.
Singh, G., Savita, K., Yadav, S., & Purwar, V. (2013). Design of adaptive noise canceller using lms algorithm. International Journal of Advanced Technology & Engineering Research (IJATER), 3(3), 85-89.
Thakkar, V. (2017). Noise Cancellation using Least Mean Square Algorithm. International Journal of Engineering Research and Application, 7(10), 46-57.
Avalos, J. G., Espinobarro, D., Velazquez, J., & Sanchez, J. C. (2009, August). Adaptive Noise Canceller using LMS algorithm with codified error in a DSP. In 2009 52nd IEEE International Midwest Symposium on Circuits and Systems (pp. 657-662). IEEE.
Dhobale, S., Boldhan, V., & Burange, R. A. (2013). Implementation of adaptive noise canceller using lms algorithm. In National Conference on Innovative Paradigms in Engineering & Technology.

## Slide 9
designed: Zeyu Liu
Thank you!
Audio Adaptive Noise Cancellation Using LMS Algorithm